## Slide 1: LSE Forecast Adjustments 2023 Resource Adequacy
Preliminary Forecasts, August 15, 2022
Lynn Marshall
Lynn.Marshall@energy.ca.gov
Energy Assessments Division
California Energy Commission

## Slide 2: Resource Adequacy Load Forecast Adjustment Process
Develop reference forecast for IOU service areas and direct access
Estimate and apply coincidence factors to LSE forecasts.
Develop reference current peak demand estimate for LSEs based on available data.
Evaluate need for LSE-specific adjustments.
Apply adjustments for incremental effects of demand side programs.
Apply pro-rata adjustments to bring the total of the forecasts to within 1% of the CEC service area forecast.
Evaluate the reasonableness of pro-rata adjustments and total forecast for each LSE and service area.
If step 7 indicates pro rata adjustment is too large (i.e., aggregate DA load significantly exceeds cap), review steps 2-7.

## Slide 3: 2021 IEPR TAC Area Coincident Peak Forecast
The reference forecast for CPUC-jurisdictional LSE forecasts begins with the forecasted monthly TAC coincident peaks from the 2021 Integrated Energy Policy Report mid-demand, AAEE Scenario 3, AAFS Scenario 3 demand forecast. The SDG&E reference forecast equals the TAC area forecast.

## Slide 4: IOU Distribution Service Area Reference Forecast Disaggregation of SCE and PGE TAC
SCE and PG&E TAC forecasts are disaggregated to CPUC and non-CPUC jurisdictional load using the IEPR service area forecasts and submitted LSE forecasts and hourly loads.
  Form 1.5b Service Area Annual (noncoincident) Peak Demand
  A top-down service area forecast is calculated by subtracting forecasted coincident peaks of pumping load and other nonconforming load from the TAC monthly coincident peak forecast. The residual monthly peaks are scaled to the IOU annual peak on Form 1.5b. A bottoms-up service area forecast is calculated by subtracting the coincident peaks forecasts of all POUs load from the TAC total. When the aggregated POU forecasts (adjusted to use the IEPR water pumping forecast) are higher than under the top-down estimate, the IOU service area forecast is reduced by using the bottoms-up approach.
  Sources:
  CED 2022 Managed Forecast - LSE and BA Tables Mid Demand - Mid AAEE Scenario 3 – AAFS Scenario 3, Form 1.5b;
  https://efiling.energy.ca.gov/GetDocument.aspx?tn=241382
  CED 2020 Managed Forecast - LSE and BA Tables Mid Demand - Mid AAEE Case, Form 1.5b
  https://efiling.energy.ca.gov/GetDocument.aspx?tn=237319&DocumentContentId=70504

## Slide 5: Comparison of RA 2023 v. RA 2022 PG&E TAC Area Coincident Peak Forecast
PGE TAC summer peak loads increase.
Time of system peak shifts later in summer months, increasing service area proportionately more than POUs, which have a higher percent of water pumping and other nonresidential load.

## Slide 6: Comparison of RA 2023 v. RA 2022 SCE TAC Area Coincident Peak Forecast
Higher recorded data starting point and lower estimated self-generation increase loads in all months

## Slide 7: Disaggregation of PG&E TAC Forecast to CPUC and POU Load
POU loads are about 10% of the TAC. With proportionately more pumping and other nonresidential load, POU loads have a flatter profile across months.
Disaggregation of PGE TAC Forecast to CPUC and POU Forecasts

## Slide 8: Disaggregation of SCE TAC Forecast to CPUC and POU Forecasts
POU loads are about 11%-12% of the SCE TAC loads.

## Slide 9: Direct Access Reference Estimate
Adjustments to ESP forecasts should be consistent with the cap on enrollment, as reflected in recent loads plus expected 2022 and 2023 increases.
Staff estimated 2023 coincident peak applying 2021 coincidence factors to estimated monthly energy expected under a full cap.
As of May 2022, SCE had not yet reached the cap. Therefore, the preliminary SCE ESP forecasts fall somewhat short of the estimated cap. ESP load forecasts will be revaluated in August using the July Direct Access Service Request data.

## Slide 10: Coincidence Adjustment Methodology
Coincidence adjustments should represent expected LSE demand at the time of a 1-in-2 CAISO-wide system peak.
Composite loads of LSEs were constructed by compiling 2021 actual loads with migrating load.
CAISO hourly loads are ranked. For each high-load hour selected, an LSE and TAC-specific coincidence factor (CF) is calculated:
  CF= LSE recorded load in TAC at time of CAISO system peak demand / LSE monthly maximum demand in TAC
  Various statistics on the distribution of CFs are calculated, including median CF of the top 3 to 5 days and percentile distribution of top 10 hours in month (excluding hours before HE 17 PST.
  Load diversity declines as demand rises, so if the most recent year doesn’t include enough relatively high load days, diversity will be overestimated, leading to increased unallocated load.
  As an alternative, staff may select the CF from the peak hour, a neighboring month, or a previous year. For example, April and May 2021 system loads were quite low, so CFs from April/May 2020, when loads and temperatures were higher, were used for many LSEs.
CAISO posts load data used for this analysis annually at: http://www.caiso.com/planning/Pages/ReliabilityRequirements/Default.aspx#Historical
Dates and times used by CEC staff are posted on the RA compliance webpage.

## Slide 11: Load Modifier Adjustments
LSE forecasts are credited with a share of net additional achievable energy efficiency and fuel substitution (AAEE/FS) and some load modifying demand response (LMDR) to the extent that it is not accounted for in their forecasts
  LSE share of incremental AAEE/FS is netted against amounts reported in their forecasts
  CEC staff reviews other load modifiers (EE, BTM PV, fuel substitution, storage, or transportation electrification) in LSE forecasts for consistency with reference forecast.
  The SCE LMDR values below also include credit for CPUC-directed procurement of front-of-the-meter storage resource in non-summer months; in the revised forecasts, the FOM storage will not be counted as a load modifier in the month of October.
  2023 Incremental AAEE/FS and LMDR Credit

## Slide 12: LSE-Specific Adjustments
LSE forecasts are evaluated using historic loads and temperatures, load factors, review of forecast assumptions, and comparison with CEC forecast assumptions
Staff uses weather-normalized loads, month-ahead forecasts, and DASR activity to construct a reference estimate for each LSE by service area:
  IOU departing load estimates are revised for consistency with CCA forecasts as adjusted by CEC, and CEC-estimated direct access load.
  Aggregate ESP forecasts are evaluated against the direct access reference estimate to identify need for further adjustments
  IOU forecasts may also be revised for differences with CEC service area forecast

## Slide 13: Pro-Rata Adjustment
If the sum of the adjusted forecasts differs from the service area reference forecast by more than 1%, the exceedance is allocated based on the share of an LSE’s adjusted forecast of total service area adjusted forecasts.
2023 Pro-Rata Adjustment Percent by TAC

## Slide 14: Summary of RA 2023 Forecast Adjustments

## Slide 15: Conclusion
  Data for these slides will be posted on the CPUC RA compliance page:
  https://www.cpuc.ca.gov/industries-and-topics/electrical-energy/electric-power-procurement/resource-adequacy-homepage/resource-adequacy-compliance-materials
  For demand forecast-related questions contact CEC staff at rafiling@energy.ca.gov