## Slide 1
September 18th, 2015
Dr. Amir Roth (DOE/EERE/BTO)
Dr. Larry Brackney (NREL)
DOE’s Energy Modeling Ecosystem
Common Platform
Data
Engines
Apps
Integrated
Services
Efficiency
Outcomes
Rapid
Consistent
Transparent
Reliable

## Slide 2: An Ecosystem: More Than an Engine or a Single Tool
Engine: Physics Calculations
Open-source & publicly-funded
Operating system: common abstractions
Accelerates App development
Open-source & publicly-funded
Apps: use-case specific
Open-source & publicly-funded
Or proprietary & commercial
Three tier architecture
Common in computer systems
Emerging in BEM

## Slide 3: DOE’s Engine: EnergyPlus (energyplus.net)
Advanced capabilities
Heat-balance method  surface temperatures, thermal comfort, radiant systems
Detailed lighting & shading, airflow within & between zones
Component-level HVAC  flexible configurations, e.g., VRF & integrated heat-pumps
Sub-hourly time-steps  cycling equipment, fast-acting systems, and controls
Scriptable controls  demand response & occupant behavior
Co-simulation
2003 R&D 100 award winner
Modern software paradigms
Open-source, transparent, and collaborative
Migrated to C++ in 2014 (thanks Autodesk!)
Rigorous software development & test processes
Full documentation
Committed federal support
$2.5M of DOE investment annually ($65M+ to date)*
In-kind contributions from Autodesk, Trane, et. al.
Two annual updates
* Just for the engine. DOE tools investments goes much further than this.

## Slide 4: DOE’s Operating System: OpenStudio (openstudio.net)
Software Development Kit (SDK)
Non-graphical “common-core” logic
  Import geometry, articulate HVAC, etc.
  Reduces application development effort
Quarterly updates
Commercial friendly open-source (of course)
$2M/yr investment from DOE & others (especially utilities)
Envelope
Constructions, loads
schedules, etc.
HVAC templates
or custom systems
Run, compare, report, QAQC, and parametric analysis
Scriptable API (C++, Ruby, Python, JS, C#)
Detailed
building
model
Application
Workflow-specific “skin”, demonstrates …

## Slide 5: Modern, Rigorous Development & Deployment
Rigorous approach to creating production software - not a research project!
Formal source management system (GitHub)
Formal task and bug tracking systems (PivotalTracker)
Automated continuous integration (CI) tests/dashboards
Formal processes for design document and code reviews
Automated documentation generation
Bi-weekly “iteration” meetings and packages
Benefits
Responsiveness to new requirements
Transparent & collaborative
Robust delivery
GitHub
Pivotal
CI Dashboard
Two
Weeks
Daily
Six
Months
Release
Features
High Priority Require-ments
Individual Tasks
Major
Releases
Minor
Releases
CI
Testing

## Slide 6: OpenStudio Killer Feature: Measures
# Measure structure to replace exterior wall orig construction with new
model.getSurfaces.each do |s|
if s.outsideBoundaryCondition == “Outdoors” and s.surfaceType == “Wall”
if s.construction.name.get_s == orig
s.setConstruction(new)
Daylighting Package
Add Heat
Recovery
Measures: scripts that operate on model & results
Transform model  apply ECM, e.g., replace constructions, daylighting package, etc.
Can be arbitrarily surgical, e.g., daylighting measure sensitive to space-type
Perform these actions repeatedly, consistently & quickly on any model
An open way of extending functionality & transferring knowledge

## Slide 7: Cooking with Gas: Measures + OpenStudio Server
ECM
ECM
ECM
ECM package optimization
Do not apply ERV
If you want this site EUI
+
Input parameter distributions
Output
distributions
EUI
But also uncertainty analysis  ranges instead of point estimates
+
And calibration  Better estimates for existing buildings
Monthly bills
Calibrated Monthly kWh
+
+
ECM
Optimizer
(EUI, ROI …)
Sampler
+
Chiller COP
Wall U Value
Optimizer
(Residuals)
Measures
Outputs
Input uncertainties

## Slide 8: Measures Are Also for Customized Reporting & QAQC
Monthly end uses
ft2 by space-type
Zone condition histogram (hrs spent in temp range)
Results Can Be
Interactive Too!

## Slide 9: Building Component Library (bcl.nrel.gov)
Online repository of measures & other model data (e.g., schedules, weather files)
Integrated with OpenStudio SDK & applications
Supports meta-data, versioning, “group” privacy/sharing & API
Browse & search on web or in app via API
Use in any OpenStudio app

## Slide 10: Technology Performance Exchange (tpex.org)
Provides OpenStudio ecosystem with component-specific data path
Equipment performance data from manufacturers, M&V’ed demos & pilots
Automated translation to BCL performance data for use in OpenStudio-based tools
Good source for uncertainty distributions  Can complement and cross-check sims
Use in any OpenStudio app
Raw performance data automatically converted into BCL objects

## Slide 11: A Relevant Ecosystem Example
CBECC-Com &
CBECC-Web
COFFEE

## Slide 12: EDAPT: Savings-By-Design Program Tracker
http://eda-pt.org
Software-guided workflow
Automated:
  Notifications
  Quality checking
  Reporting
  Portfolio roll-ups
Integrated with OpenStudio
Can be integrated with other tools
Developed for Xcel Energy
  Saved $500k in program admin costs in 1st year of operation
  Grew from 2 consultants to 10
  Significant increase in number of projects processed annually
Now available to other utilities

## Slide 13: Ecosystem: Online Reference & Learning Resources
http://energyplus.net/
Downloads & example files
Training videos & step-by-step tutorials
http://openstudio.net/

## Slide 14: Ecosystem: Online Q&A and Feedback Resources
http://unmethours.com/
http://energyplus.uservoice.com/
http://openstudio.uservoice.com/
Peer-to-peer Q&A site
800+ users, 150+ questions/month
Development teams and users active
User feedback sites
New feature proposal, discussion & voting

## Slide 15: Key Strengths of the DOE Ecosystem
EnergyPlus’ Advanced Modeling Capabilities
Correctly models physics and technologies needed to achieve high efficiency targets
Commercial-Friendly Open-Source
  Transparent source code, reference data & engineering assumptions
  Transparent development process & roadmap
  Enables and accelerates market innovation
"Free software is a matter of liberty, not price… think of free as in free speech, not as in free beer.”
- Richard Stallman

## Slide 16: Key Strengths of the DOE Ecosystem
EnergyPlus’ Advanced Modeling Capabilities
Commercial-Friendly Open-Source
Cost-Shared, Continuous Development
DOE invests heavily to maintain the platform as a public good
Third-parties are augmenting this investment
  Autodesk C++ conversion
  Trane and Carrier in-kind HVAC improvements & validation
  Utility investment in OpenStudio, EDAPT & measure content
Chart: 
| FY10 | FY11 | F12 | FY13 | FY14 | FY15
DOE | 1950 | 1050 | 1770 | 1652 | 1233 | 1205
Cost Share | 333 | 423 | 923 | 1490 | 1522 | 1050
OpenStudio Budgets
Chart: 
| FY10 | FY11 | F12 | FY13 | FY14 | FY15
DOE | 4000 | 4000 | 3000 | 3000 | 2600 | 3000
Cost Share | 0 | 0 | 200 | 200 | 350 | 350
EnergyPlus Budgets

## Slide 17: Key Strengths of the DOE Ecosystem
EnergyPlus’ Advanced Modeling Capabilities
Commercial-Friendly Open-Source
Cost-Shared, Continuous Development
OpenStudio Measures Are Now a Common Currency
Codifies and distributes best practice
Enables automation for lower cost & greater reliability
Many firms are now able to add capability to the ecosystem
Help!
Ich bin expert!
Thanks!

## Slide 18: Key Strengths of the DOE Ecosystem
EnergyPlus’ Advanced Modeling Capabilities
Commercial-Friendly Open-Source
Cost-Shared, Continuous Development
OpenStudio Measures Are Now a Common Currency
Scalable solution for big problems
  Design optimization
  Calibration
  Uncertainty and sensitivity analysis
  Portfolio-scale potential studies & EE Targeting
Custom
Analysis
Tech Potential
Analysis
Identical Assumptions &
Modeling Approaches
Reference
Models
EE Measures