## Slide 1: Demand Response and Local RA Criteria Discussion
2016-02-18

## Slide 2: There are methods for DR resources with response times greater than 20 minutes to meet local RA requirements
CAISO’s Clarified Criteria for Local DR Eligibility:
A resource must be capable of (1) responding within 20 minutes or (2) being available for a sufficient number of pre-dispatches (i.e. starts per month) to count toward local capacity requirements.
Approximately 600 MW of DR located in local areas would not be eligible for Local RA if only programs with a 20 minute response time were eligible. However, SCE is determining how much DR from other programs will be available to meet local RA criteria by studying:
  The number of pre-dispatches required for resources to count towards local RA (currently in progress)
  The ability of DR resources with contractual response times greater than 20 minutes to realize energy reductions within 20 minutes (as load ramps down to meet the longer duration requirement).
Local Area Demand Response MW and Contractual Response Times
Local Area | Less than 20 Minute Response Time | 30 Minute Response Time | Greater than 30 Minute Response Time | Day Ahead Dispatch
LA Basin | 321 | 379 | 107 | 28
Big Creek / Ventura | 154 | 57 | 27 | 4
Total MW | 475 | 436 | 134 | 32

## Slide 3: Historical BIP-30 dispatch shows that up to 281 MW could be obtained within 20-minutes from a 30-minute program
Base Interruptible 30-Minute Response Program (BIP-30)
Example Performance based on Historical Dispatch Data
Local Area | Total MW |  | Historical Dispatch 0-15 Minute Response | Historical Dispatch 15-30 Minute Response
LA Basin | 379 MW |  | 244 MW | 322 MW
Big Creek Ventura | 57 MW |  | 37 MW | 49 MW
Total Local Area | 436 MW |  | 281 MW | 371 MW
Using data from an actual dispatch, up to 65% of a 30-minute programs local capacity may be eligible to provide 20-minute response in local areas.
This example is based on a single program’s performance in one day, to find the actual amount of 20-minute response that can reliably be provided:
  Analysis will need to be based on more than a single day’s dispatch results
  Analysis will need to take into account potential lag time between a CAISO dispatch and resource performance (e.g., time for SCE to notify DR participants to reduce load) and measurement period limitations.
Results are not final and are for discussion purposes only

## Slide 4: Next Steps
SCE is planning on submitting this proposal during the March 11th “Optional Revisions to Proposals” filing
For questions and comments, please contact:
  Martin Blagaich
  Martin.Blagaich@sce.com